Indoor Navigation with Arduino
– helping lost students appear on time

---
Goals
- Design of a web app which displays the user’s position and shows direction to the selected room inside the building
- Localization based on sensor/uC data
  - Displacement and orientation
- Design of the web app
  - Live display of sensor data

---
Orientation
- IMU = accelerometer + magnetometer + gyroscope
- All can be used for orientation
  - Accelerometer works with gravity:
    - When flat, a = (0,0,g)
    - (ax, ay, az) measured after three rotations → back conversion for rotated angle
  - Magnetometer values also calculated after rotations
  - Gyroscope measures angular speed
- Difficulties:
  - Accelerometer is noisy, while gyroscope drifts → complementary filter
  - Effects of tilting makes measuring while moving difficult

---
Orientation
A working approach (if any)

---
Displacement
- Displacement with double integration
  - v += a*dt, s += v*dt
- Very difficult in reality
  - Tilting of the sensor has to be compensated
    - difficult when the user is moving
  - Movement detection
    - Set v to zero if the user is not moving
  - However, nothing prevents the noise from being integrated and screwing the results!

---
Displacement
- A new use of accelerometer: step detector
- Assumptions

---
Displacement
- An improvement: Wi-Fi fingerprinting
- A ML based approach: kNN (k nearest neighbours)
  - Each node has a label
  - L2 distances between node x and all other nodes are computed and the k nearest neighbors vote on the label of node x.
- Application:
  - The map is divided and labeled
  - Vector of signal qualities (0-70) to different APs used as metric
  - L2 distance computed from the signal quality vectors

---
1. The code in Github implements the approach I found https://www.nxp.com/docs/en/application-note/AN4248.pdf, failure might be due to the exchange of x & y axis